Product Specification

Product Name	Colt Proteus Louvre type PR 100

Manufacturer	Colt Ventilation East Asia Pte

Louvre profile	Single Bank extruded 100 mm pitch

Construction 	Quality corrosion resistant aluminium alloy

Louvre blades shall not be drilled but clipped and not riveted or screwed to structural supporting mullions allowing for expansion and contraction along their length without distortion and to provide a continuous external appearance if required.

Mullions shall be concealed at 1250mm maximum centres and their points of support along their length shall be in accordance with prevailing site wind pressures (as calculated and specified by a structural engineer).  Manufactured from 2mm sheet such that associated support steelwork is reduced to a minimum.

Cills and frames 	Shall contain all peripheral fixings

Corners		Extruded mitre corner pieces / mitred cut

Paint Finish	Partially coated / totally coated  to any RAL polyester powder colour
Partial / total finish
Anodised finish

Guards		Insect / bird / security

Optional extras	Acoustic modules
				Blanking panels (single skin or insulated)
				Louvre doors
				Roof turrets

Fixing	The ventilator is designed to be fitted into an opening and/or supporting members supplied and fitted by others.