Product Specification

Product Name	Colt Proteus Operable Louvre

Manufacturer	Colt Ventilation East Asia Pte

Louvre profile	Single Bank extruded 100 mm pitch

Construction 	Quality corrosion resistant aluminium alloy. Comprising 1.5mm thick extruded louvre blades centrally pivoted on nylon bearings with an aluminium box section surround frame.

Cills and frames 	Shall contain all peripheral fixings

Corners		Extruded mitre corner pieces / mitred cut

Paint Finish	Partially coated / totally coated  to any RAL polyester powder colour
Partial / total finish
Anodised finish

Guards		Insect / bird / security

Optional extras	Acoustic modules
				Blanking panels (single skin or insulated)

Fixing	The ventilator is designed to be fitted into an opening and/or supporting members supplied and fitted by others.

Controls	Manual, electric or pneumatic

Performance

Test data is for the unit in the open position only

Airflow 		Air Inlet - 0.37 (including bird guard)

Air Extract - 0.45 (including bird guard)

Rain defence	Class A2 - up to 0m/s suction velocity

Class B2 - up to 1.5m/s suction velocity
Class C2 - up to 2.0m/s suction velocity
Class D2 - up to 3.5m/s suction velocity